BRICK HOUSE: ELECTRONICS

Electronic

outfitting

for o ur

circumnavigation

he electronics on our

ation, integration of the electronics.

finally reaching the boating world.

52

boat were all top of

the line 15 years ago.

Replacing them is

like throwing away

a perfectly good eight-track tape

player and installing a new MP3

player. Choosing new equipment

for our circumnavigation on Brick

House, our 1976 Valiant 40, I had

to make the same considerations

as the previous owners so our new

electronics will also be performing

15 years from now. This included

power draw, reliability, cost, cus-

tomer service outside of the United

States and the newest consider-

Some people would say our boat

is “decked out.” I would say it is

sensibly fitted out for a couple with

some resources to do things right,

without wasting money and making

things terribly complicated.

DEPTH SOUNDER AND SONAR

First came the primary naviga-

tion instruments—the depth, speed

and wind. It is important above

all else that depth is correct, and

dependable, particularly in the shal-

low places we will be visiting, such

as the Bahamas. Everything in our

life is going wireless and the trend is

Our Tacktick wind instruments

eliminate all the inherent problems

with wires inside the mast. Screw

down the masthead unit, calibrate

the solar powered display and you

have wind instrumentation. The

wireless, solar charged display runs

for days with just a few hours of sun

even on a cloudy day.

The Tacktick depth and speed are

typical wired transducers that feed

to a transmitter. The transmitter

can be mounted anywhere in the

boat as long as it is not blocked by a

large metal object. What few wires

there are connecting the transducer

Blue Water Sailing • January 2008

and transmitter are color coded

and well labeled. It did not take

Being a low

power system,

my computer background to make

those connections. The transmitter

must be charged from the 12-volt

system or an optional small solar

panel, but it draws less than five

amps over a 24-hour period while

switched on, and it does not need

power continuously.

There is a simple, well document-

ed startup procedure that networks

all of these instruments so that the

user can cycle through most of the

wind, depth and speed information

the Tacktick

depth sounder

on our boat is

accurate to just

over 100 feet.

For the occasions

when we care

to read greater

water depths,

we installed a

Lowrance LMS-

525C DF sonar/

fish finder, which

Raymarine C80

on any of the displays. I actually

had this part completed on a snowy

day on my dining room table, 15

minutes after I received the box.

The only issue we have had is with

the wind display. We have a large

array of solar panels mounted on

a hard dodger, which degrades the

signal from the mast. To help iden-

tify this signal restriction, Tacktick

has a network health function. The

function displays signal strength

from zero to six, with six being the

strongest. Moving the wind display

from underneath the dodger to a

simple mount on the steering ped-

estal improved the signal. With the

display in clear sight of the mast,

the strength shot up to five.

Tacktick instruments

Blue Water Sailing • www.bwsailing.com

has a depth range to 2,500 feet. The

sonar is so powerful that its signal

will overwhelm the Tacktick depth

display and upset its reading. The

color sonar gives us a representation

of the density layers of the seabed

below our keel, the contour of the

bottom, as well as any free swim-

ming lunch that may be in the area.

The sonar transducer contains a

probe for water temperature so we

can tell when we are entering and

leaving currents or an upwelling.

This unit also has chartplotting

capabilities, which makes it another

back up navigational tool. We are

keeping the sonar as a stand-alone

item and see no reason to interface

it with other instruments.

Our

old laptop

computer

and a simple

chartplot-

ting program

have served

well when

delivering

other peoples

boats. What a

few years ago

seemed state

of the art

will now go

to a storage

locker on our

boat as back-up equipment. All of

today’s chartplotters are far more

energy efficient, user friendly and

quite frankly, more reliable than the

average laptop.

CHARTPLOTTER

I chose Raymarine’s C80 Chart-

plotter with their Raystar 125 GPS

antenna for many reasons. First,

Raymarine’s customer service is very

highly rated. Second, the Ray-

marine C80 uses Navionics chart

cards. Each Navionics card covers a

huge area so there aren’t many cards

needed to complete a circumnaviga-

tion, making it more economical.

The charts show all the standard

buoy and navigational information

plus points of interest, facilities in

each harbor including contact and

amenities information, tide and

current data and many other useful

items. The Raymarine C80 further

takes advantage of these abilities

displaying current, wind and head-

ing vectors. With a special patented

Navionics card reader, I can also

use the Navionics charts in my

spare PC with various chartplotting

programs. I chose the Fugawi chart-

plotting software for the laptop

because it has all the capabilities we

need, including an AIS (Automatic

Identification System) display, for

an affordable price.

53

BRICK HOUSE: ELECTRONICS

The C80

display

easily fit in

a predomi-

nant spot in

our nav sta-

tion, and is

even view-

able from

the cockpit,

course.

MARPA

will tell

the user

the CPA

(Closest

Point of

Ap-

proach)

and

which

avoids the

adherent

prob-

lems with

installa-

AIS information displayed on

the Raymarine radar

TCPA

(Time to

Closest

Point of

Ap-

proach).

54

tions above deck. If we had a larger

budget, we would have gone with

the C120, which has a larger screen

making it even easier to see from

the cockpit.

The installation of the Rayma-

rine chartplotter is easy. Follow the

simple instructions and you can’t

go wrong. I ran power cables from

a dedicated circuit breaker on the

electric panel to the C80. SeaTalk

and NMEA cables were plugged

into the back of the C80 unit and

then to a Brookhouse multiplexer.

The multiplexer is the hub that

brings all the other instruments to-

gether for integration. The only in-

stallation issue we had was with the

Raystar 125 GPS antenna, which

brings the satellite signals into the

C80. It can be used for NMEA or

SeaTalk, but you have to physi-

cally tell the chartplotter which one

of these languages to listen for by

including or not including a green

wire with the red power cable. It is

the only important detail not high-

lighted in the manual.

After installation, the chartplot-

ter has worked flawlessly with

extremely low power demand.

There are some add-on features that

we did not opt for. Sirius Satellite

Weather and radio would be great if

it extended internationally. The fish

finder add-on looks like a nice en-

hancement, but we wanted a com-

pletely isolated system for this. We

did however, add the radar option

when we saw how it could be split

on the screen with the chart plotter

or instrument page, or overlaid

onto the chartplotter screen. The

C80 unit uses less than one amp to

run the chartplotter and a total of

less than four amps with the radar

transmitting. This is less than half

the energy that our old radar alone

consumed. Now we use the radar

liberally, rather than turning it on

with hesitation like we did with the

old unit. Having this information

available quickly adds safety to our

boat. Some independent tests show

that our Raymarine two-kilowatt

radar outperforms the four-kilowatt

units from other manufacturers.

Kilowatt power is theoretically

related to signal return and how

well targets display on the screen.

Larger kilowatt units also require a

larger antenna, which becomes an

installation problem on a 40-foot

sailboat, and demands more battery

amperage.

Our Raymarine radar came with

the MARPA (Mini Automatic

Radar Plotting Aid) feature. It au-

tomatically tracks targets, calculates

their bearing, range, speed and

I like and use the feature. Patrick

feels his eyes can do a better job of

tracking targets on the radar, espe-

cially small or other targets that are

intermittently obscured by waves or

weather.

AIS

One thing that shows up very

well on the radar and chartplotter

screen is the ship sign indicating

an AIS target. I bought the $160

SR161 Millitech AIS receiver. The

receiver gets its signal split off from

a standard VHF antenna. The

receiver connects to a special AIS

port in the multiplexer. Traveling

down the narrow East River of New

York City, in the fog, it was great to

know that around a blind bend be-

hind us was a ship coming toward

our stern at 8 knots, drawing 14

feet and with 40 feet of beam, and

that up ahead in the fog there were

three tugs and a large yacht that

had all come to a stop in mid river.

It would be impossible for radar to

see any of those vessels. AIS range is

far greater than our eyes or that of

the radar. Even in good weather it

is fun to put the cursor on the ship

in question to see if it was moving

in a way to be a threat to our course

or not. The installation of this little

four-inch by three-inch black box

Blue Water Sailing • January 2008

was straightforward, but its integra-

tion was not simple at first. All the

other instruments on board use a

4,800-baud rate. This one uses a

38,400-baud rate. The Raymarine

C80 display has only one NMEA

port…so only one baud speed.

There was a solution

though!

MULTIPLEXER

The solution was the

multiplexer made by

Brookhouse. This little

black box coordinates

the different languages

and baud rates of the

various instruments so

that all of the instru-

ments can understand

each other. They have

a unit specifically for

the Raymarine C and E

series units with SeaTalk,

NMEA 0183 and an

RS232 or USB port so it

can communicate with

your laptop too. You can

even have a loud external

alarm added to it, pro-

grammed to sound when

a certain criteria is met

on any of your NMEA

instruments. Each port is

programmable for a dif-

ferent baud rate includ-

ing one preprogrammed

for AIS. Everything is

labeled for easy instal-

lation. I struggled for

days to understand how

to exactly use this little box, but

Brookhouse support, and some pa-

tience on my part, made it all come

together. The Brookhouse mul-

tiplexer device, along with Tack-

tick’s NMEA interface, makes our

Tacktick instruments integrate with

everything as well. The portable

Tacktick displays can show Rayma-

rine’s information and vice versa.

Blue Water Sailing • www.bwsailing.com

At Sandy Hook, N.J., we were

anchored in a storm, and I brought

one Tacktick instrument to bed

with me to look for SOG (speed

over ground), depth and wind in-

creases whenever my eyelids opened

with worry, instead of getting up to

look 100 times that night!

AUTOPILOT

Part of our new electronics pack-

age was the autopilot. We wanted

an oversized powerful autopilot to

use when we are not in a position to

use our Monitor self-steering wind

vane, like when motoring. If we

ever lost our 30-year-old pedestal

steering, the autopilot would take

over as our back up steering. Our

boat has a displacement of 22,500

pounds. The Raymarine specifica-

tions call for a Type 2 short (T2S)

Linear Drive to accommodate a

boat up to 33,000 pounds of dis-

placement. We wanted

overkill and opted for

the Type 2 Long (T2L),

which is specified for

boats up to 44,000

pounds displacement.

The Controller is the

small box in the cockpit

with buttons for con-

trolling the direction of

the boat. We chose the

simplest controller with

the least user options,

the ST6002 and the

SG3 Course computer

with built in Gyro and

AST (Advanced Steering

Technology). It seems

like everyone integrates

their autopilot with their

chartplotter…we may be

the only ones who have

not. Too much trust in

electronics can be a bad

thing. Manually chang-

ing the course 10 degrees

coupled with a look at

the horizon is so much

easier than steering by

hand. How easy do we

really need to make it

before all of these elec-

tronics become a liability

rather than an asset?

SINGLE SIDEBAND

The other electronic device I

spent a lot of time working on was

our SSB/Ham radio. It is an older

Icom 710 RT. The SCS Pactor

III Modem and SSB handles our

e-mail and weather reports. The

previous owner had reported using

the SSB and his modem with great

55

BRICK HOUSE: ELECTRONICS

time I need them. This means

no getting up at 3 a.m. to get

scheduled weatherfaxes if the text

reports are adequate for me at the

time. It is nice to have the report

in writing, as sometimes at sea it

is hard to hear and decipher what

they are saying on a voice report.

INTERNET ACCESS

When we are in an anchorage

surrounded by suburban build-

ings, or near a marina, I can get

Internet access on our boat with

a WiFi card in my laptop. I have

two types of antennas to capture

the wireless signal. The Cantenna

200mW long-range USB adapter,

which is attached to my laptop via

a 15-foot USB cable. WiFi, when

available, makes the retrieval of my

e-mail and weather faster by means

of telnet to SailMail, as well as

giving me the usual convenience of

Internet browsing.

We have three laptops onboard.

One for word processing and

camera functions that never sees

the Internet. Another is specifically

for the Internet and SailMail and

is protected with virus and spyware

software, and has all of the lat-

est updates. Then we have a spare

laptop that is well waterproofed

56

success, but when I finally bought

my new modem to get e-mail and

weather through SailMail and Win-

link, I was disappointed to not be

able to connect to the service at all.

I had expert advice, which proved

to be completely wrong, and then

new advice that finally put me on

the path to high power and clear

reception. Describing in detail the

modifications that got me commu-

nicating with the world would take

enough words for another article.

In short, the biggest modifications

were adding copper grounding, and

replacing wire grounding connec-

tions with strap connections.

Now I am getting a reliable, rela-

tively fast connection to download

weather reports via Saildocs, my ra-

dio e-mail via SailMail (commercial

SSB) and Winlink (Ham), as well

as my land-based e-mail via a newer

feature of AirMail called “Shad-

owMail.” ShadowMail enables me

to query my Yahoo server, or any

other POP e-mail server, for e-mail

in that account. I can then choose

which ones to download.

I can get weatherfaxes through

the radio via the Pactor modem at

their scheduled times, as well as text

weather reports and GRIB files any

directional antenna strapped to the

boom pointed in the direction of

the strongest signal gives us a good

signal far out in an anchorage. The

other antenna is an omni direction-

al. Sometimes there is no predicting

which antenna will work best in an

anchorage. I bought both antennas

at our local Radio Shack electron-

ics store. One of these is connected

to my EnGenius EUB-362EXT

AirMail screen showing weather options

and packed away for use for backup

navigation, and SailMail. All of

them are at least five years old. The

newest laptops consume too much

electricity, and laptop survival on

a boat is too short to be worth the

cost.

BATTERIES

There are two or three other

components of our total system that

Blue Water Sailing • January 2008

The Cantenna directional antenna

I need to mention. They are the

“muscles” that make the rest of the

electronics work. We have a battery

bank of six six-volt Trojan lead-acid

batteries. They amount to 675 amp

hours. This computes to less than

235 usable amps in actuality, if

you subscribe to not draining your

batteries beyond 50 percent of their

amperage capacity, and not charg-

ing above 85 percent since that last

15 percent takes so much resource.

Previous owners of this boat had

given a lot of thought to battery

charging and installed three 65-watt

Kyocera solar panels. After 15 years

the panels are still doing their job

putting out 60-70 amps per day.

The wind generator spins and

sounds like an unbalanced Cessna

150 engine and

power back

into the bat-

teries.

DECKED

OUT?

Are we

decked out?

I don’t think

so. Today’s

electronics are

a great source of affordable safety

information not dreamed of 15 or

20 years ago. We have informa-

tion coming in from high quality,

reliable electronics, so we can make

prudent decisions. With finite

resources, we kept our cruising kitty

intact rather than upgrading be-

yond our means. By installing this

equipment

ourselves,

and keeping

it as simple

as possible,

we will be

self-sufficient

and hopefully

not spending

a lot of time

in ports wait-

ing for parts and repairing the boat.

Most importantly, we are confident

this same equipment will be operat-

ing faithfully for new owners, 15

years from now.

Patrick and Rebecca Childress have

restored their 1976  Valiant 40 and

recently left on their circumnavigation.

puts out no am-

perage at all until

there is a 15-knot

breeze, and it

takes 25 knots

of wind to really

produce sufficient

amperage. We

are looking into

newer, more tech-

nically advanced

wind generators

that need less

wind to produce

more power.

When our diesel

engine is run-

ning, the Balmar

150-amp, high-

output alternator

does a fairly quick

job of putting

65-watt Kyocera solar panels

Blue Water Sailing • www.bwsailing.com

57