Two Years and

Cruising

What Has Worked

and What Hasn’t

www.bwsailing.com

53

FITTING OUT FOR WORLD CRUISING

ailing away from Rhode

held in place with a keyway and

ing. In Panama, the rebuild was

54

Island and now cruis-

ing deep into the South

Pacific, two years have

passed in a blink. Re-

becca and I have been treated to

high adventures, lush mountainous

landfalls and skill-testing coral atolls

to navigate.We now recognize that

our initial thoughts of a four year

circumnavigation on our Valiant 40,

Brick House, was an impractical goal;

a six-year plan seems more realis-

tic. Brick House is up to the task,

but thinking of the equipment we

installed on board before watching

New England fall below the hori-

zon, there are some items that have

worked out better than others.

On the plus side, some boat

systems are so reliable that we don’t

think about them at all, yet it would

be an instant disaster if they failed.

The autopilot tiller arm attached to

the rudder post is one hidden piece

of vital equipment. Our Edson tiller

arm is a massive piece of bronze

heavy bolts clamping it to the rud-

der post. Once in a great while I

contort my way down into the aft

compartment of the boat to inspect

the tiller arm, autopilot linear drive

and all the steering cable linkages.

The tiller arm remains rock solid.

In Honduras, I witnessed what can

happen to a less beefy tiller arm. On

a 46-foot boat that had managed its

way through some rough weather,

the tiller arm had sheared its mount-

ing bolts and bent the arm itself.

There is a difference in how such

forgettable pieces of equipment are

manufactured.

Our Edson hand bilge pump is

another piece of equipment that is

strong and reliable; like the life raft,

we see it every day but fortunately

have not had the opportunity to

use it.

FORM FOLLOWS FUNCTION

After a year and a half, our old

150-amp alternator stopped work-

quick and inexpensive. The new

brushes failed again three months

later. Our backup 45-amp alterna-

tor was only a crutch that could not

keep up with our energy demands.

This taught us that a backup piece

of equipment should be equal to

the primary. In Tahiti we installed a

new 120-amp high output alterna-

tor called Powermax. “More amper-

age at a lower engine rpm!” was the

hype. It has performed better than

our old 150-amp alternator, but this

is accomplished in part by install-

ing a smaller diameter pulley, thus

increasing the rpm of the alternator.

In doing this, it takes more power

from the engine and places a greater

stress on the single fan belt, caus-

ing premature wear of the belt. The

smell of burning fan belt rubber

and a climbing engine temperature

added to the excitement of our

last-second aborted approach at the

entrance to the narrowest, strongest

flowing, most wave-washed channel

Blue Water Sailing • november 2009

of all the coral atolls in the South

Pacific. A boat project upon reaching

New Zealand will be to add a second

fan belt to our high output alterna-

tor. We will also order “rebuild kits”

for our alternators so we

can replace the brushes

and other easy-to-in-

stall parts on our own.

It is my fault for not

insisting it be made

right, but we were get-

ting a good deal and

I thought I could live

with it. The new main

halyard and reefing

lines, which lead to the

cockpit, arrived from

the rigger, being all the

same color. The differ-

ence was the number

of tiny blue yarns on

each line. This is not a

quickly recognizable

distinction. True, we

now know by feel where

a particular line and its

ber with a peel-away backing exposing

the sticky adhesive. In two years, not a

drop has trickled down the mast.

On deck, half of our teak handrails

were removed and replaced with

drives me to do something more in-

teresting, like go outside and polish

stainless steel until net time is over.

The cruisers’ nets do have strong

merits, however, and there were two

brake are located, but I

Sometimes items that are easily forgotten about, such as the Edson

am sorry I did not insist

on the lines each being

a solid and different

tiller arm, can be the most important. Labeled rope clutches are

necessary when your lines are nearly identical

times I did a

U-turn from

the compan-

color. The neat-looking splices on

the shackle end of the halyards are

so long and bulky that they ride over

the masthead sheave or spinnaker

halyard block and have been sliced

through by the sharp edges of the

blocks. I have swapped the halyards

end for end and simply tied the hal-

yard to the shackles with a bowline,

which does not interfere with other

hardware.

In Rhode Island, function out-

weighed cosmetics when I decided

to put a stop to the leak at the mast

boot. I had installed some rubber

roof membrane over the existing

boot. The material is thick, black rub-

what we thought would be lower

maintenance, better looking stain-

less steel. Rather than varnishing, we

now spend time polishing stainless

to remove rust. Fresh water and soap

is what stainless steel likes best to

remove salt and grime. Without that

flushing, which rarely happens on

a cruising boat, stainless steel soon

turns to yellow steel. The remaining

teak handrails, which were sanded,

primed and painted, look as glossy as

the day we sailed south.

Rebecca loves to talk on the single

sideband radio and often serves as

a “Net Controller” for the morning

cruisers’ net. All that frivolous chat

ionway to listen to the radio with

wide ears. One lone sailor was lost

after leaving Key West on a beauti-

ful 46-foot sailboat. His two-week

adventure was a daily soap opera

for the listeners of the Northwest

Caribbean Net. Because of the advice

and concern of listening cruisers, the

saga, for now, ended when he landed

safely on the island of Roatan in the

southwest Caribbean. In the Pacific,

a sailing couple on the yacht Avatar

called into the “Coconut Net” when

the hollow pipe shaft of their spade

rudder broke away, 900 miles east of

American Samoa. The closest help

available would pluck them from

www.bwsailing.com

55

FITTING OUT FOR WORLD CRUISING

It may not be pretty, but the black

rubber membrane keeps water

from dripping down the mast, left.

The $25 SSB antenna solution,

above

56

their yacht, but would do nothing

to help rescue their floating home.

Rebecca and I were anchored at a

coral atoll 230 miles upwind from

the distressed yacht. We delivered,

mid ocean, the emergency lumber

requested so Avatar could fashion

a new steering system and limp to

American Samoa. Even if a cruiser

does not talk on the SSB nets serving

a cruising route, it is worth making

a list of the frequencies so you can

listen in and become familiar with

the radio procedures. Our SSB, cou-

pled with a Pactor modem, continues

to be invaluable for communication,

weather and maintaining our busi-

ness affairs from afar.

RIGGING, DINGHIES

AND MORE

Polishing stainless steel one morn-

ing, I found a severely cracked swage

on the backstay. We were able to

hold the backstay together by clamp-

ing two sets of block and tackle

above the bad swage and the lower

ends attached to the chainplate.

Replacing the backstay, we decided

to eliminate the weight of the two

expensive insulators that allowed

the stay to serve as our SSB antenna.

This also eliminated four swages,

which were additional failure points.

Our new SSB antenna is simply a

stainless steel wire, smaller than

what would be used for a lifeline.

Swaged with plastic thimbles at both

ends, the wire was secured with a

strong line so it is four feet from the

masthead. This is so the mast will

not shield the antenna, reducing its

performance. The bottom end of

the wire antenna is tied several feet

away from the backstay and a foot

up from the cockpit arch so it is out

of reach from anyone standing at the

back of the boat. The $25 antenna

works so well that for now, we have

no reason to change it.

After our backstay surprise, we

now carry on board a new spare

stay equal to the longest stay on the

boat. The upper end has a swage eye

already installed. The lower end can

be cut with a hacksaw and finished

with a manually-installed swageless

compression fitting.

Another rigging problem we had

was the removal of corroded set

screws from the jib roller furling sys-

tem so I could adjust the turnbuckle

and inspect the lower terminal end

of the headstay. It is now a scheduled

maintenance item to remove and

grease those set screws. In remov-

ing one set screw, I broke an Easy

Out screw extractor. In my toolbox,

I should have doubled the number

and increased the variety of sizes of

these screw extractor tools.

It was good advice when we heard,

“Get the largest dinghy you can carry

on deck with the largest engine pos-

sible.” Our V-hull Avon RIB (Rigid

Inflatable Boat) with a fiberglass

bottom has been nearly perfect. I

now think that I should have cashed

in more used cans and paid the big

difference for an aluminum hull RIB.

The weight savings is great, which

would make it easier to winch the

dinghy on deck with the spinnaker

halyard. An aluminum hull will

merely scratch and dent where our

fiberglass hull is sporting nicks and

dings from reef and rock bites.

We were adamant about putting

a two-stroke, 15-horsepower en-

gine on the transom of our dinghy.

We bought the engine in Nassau,

Bahamas. The immediate benefits

over a four-stroke engine are greater

horsepower-to-weight ratio and

ease of handling when lifting onto

and off the dinghy by means of a

Blue Water Sailing • november 2009

block and tackle hoist at the stern

of Brick House. For a far ranging

cruising yacht, a huge advantage

of a two-cycle engine is the ease of

maintenance. In a beautiful cove on

the island of Nuka Hiva, Marque-

sas, French Polynesia, I returned

to the beach to find the surf had

flipped the dinghy upside down.

The power head of the engine was

being ground into the black sand

beach, the outdrive waving in the

air pleading for help. Bailing out the

dinghy and returning to Brick House,

it took one hour and two pulls of the

starter rope for the engine to roar to

life. To clean the dust-fine clods of

sand from the fuel system, cylinders,

flywheel and especially the oil cham-

bers of a four-stroke engine would

have been exponentially more dif-

ficult. On a four-stroke engine, there

could be catastrophic residual effects

if every speck of grit and water could

not be removed from the oil-filled

crankcase. Our two-stroke Mercury

outboard brushed off the incident

and hasn’t looked back.

To get our nine-foot dinghy up on

a plane faster and to be able to plane

at a slower engine rpm, we bolted

what amounts to wings (sometimes

called “hydrofoils”) to the cavitation

plates. However, when the dinghy

is lightly loaded, at high speed the

hydrofoils produce an undesirable

bow-down attitude.

One reliable item that is used

every day is the inexpensive Jabsco

head. In two years we replaced one

pump O-ring. That O-ring likely

deteriorated because of the clean-

ers we put through the head. In the

80-degree water of the southern

Caribbean and equatorial Pacific, I

would have to occasionally put a few

drops of vegetable oil in the pump

cylinder to quiet the squeak of the

piston O-ring. Now that we are in

www.bwsailing.com

cooler ocean water well south of the

equator, inexplicably, the O-ring has

needed no additional lubrication.

In New Zealand, I am looking

forward to hauling Brick House from

the water to throw on another coat

of antifouling paint and at the same

time possibly install a feathering

prop to replace our three-bladed

fixed propeller. We would also like

to install an AIS transponder so our

little boat will show up as a ship on

everyone else’s AIS receiver.

One thing that has worked un-

expectedly well is the economics

of the cruising lifestyle. In the last

two years, we have bought no home

heating oil and paid for no electric-

ity from the municipal power plant.

The gasoline we put through our

outboard engine in three months is

far less than what my Ford Explorer

drank in a week. In Rhode Island, it

would have taken weeks of working

at a profession to make the mort-

gage payment and just to exist. We

spend money on educational tours

of new islands and books on fish and

bird identification, but we seldom

eat in restaurants. There are days we

do work long hours, but it is in clear

water stalking fish and lobsters for the

freezer. We pick fruit from the trees

and trade for vegetables. Overall, life is

a cruise and we wonder how the past

two years have slipped by so quickly.

57