BRICK HOUSE: AUTOPILOT

Installing the

Autopilot

ut of the black

Careful installation will

ensure years of service

from your “third crew

member”

by the autopilot. There would be

50

sliced a strong, chill

wind, blowing the

Swan 46 downwind

at seven knots.

Bermuda was 200 miles ahead as

Rhode Island quickly slipped more

than 440 miles from the stern.

Huddled behind the wheel, spray

sounded like pebbles sprinkling the

plastic of my foul weather hood

pulled tightly over my head. Sud-

denly the companionway hatch flew

open spilling light into the cockpit

and hammered a pounding into my

startled heart. I had been so relaxed

enjoying the ride but now had to

jump to the wheel.

The crewman plopped into the

damp cockpit and asked how things

were going. I made it look so easy

to talk and casually hold a precise

course. Actually the autopilot was

moving me and I was cheating by

using it. It was no longer my turn

but I could not let the new watch

take the helm and discover my

secret. Fortunately we both agreed

the jib needed a slight adjustment.

With that opportunity I hit the

standby button and slipped the

sun cover over the controller. I was

the captain but I wanted everyone

on board to be fully competent at

hand steering and not be enticed

plenty of time south of Bermuda

to learn how to steer a boat to the

Caribbean by merely pushing a few

buttons. As on most passages, this

boat would never steer a straighter

course than when the rudder was

under control of the autopilot. As a

delivery captain I have used many

Raymarine autopilots, and Ray-

marine is what my wife and I have

chosen to steer our Valiant 40, Brick

House, around the world.

There are five main components

to an autopilot: The course com-

puter, controller, drive mechanism,

fluxgate compass and the rudder

position sensor.

Course

Computer

Raymarine’s

S3G course

computer (Fig-

ure 1)is the brain

of the autopilot.

The course com-

puter receives its

heading infor-

mation form

the remotely

mounted flux-

gate compass.

The fluxgate

compass gives

the rocking and rolling of the ves-

sel due to the Gyro (stabilization)

technology used with the S3G

computer system. The S3G also has

what they call “AST,” which is short

for Advanced Steering Technology,

with an auto learn ability. The unit

actually gets to know the steering

habits of your particular boat, and

adjusts over time accordingly. In

short, we chose the S3G because

it is at the top in brainpower and

can handle many functions when

programmed to do so.

Drive meChanism

The drive mechanism (Figure 2)

is the muscle that moves the rudder.

Figure 1

Blue Water Sailing • December 2007

Figure 2

Initially I wanted a hydraulic drive

as those units always worked flaw-

lessly on the larger boats I delivered.

However Raymarine Pre-Sales

support convinced us that service

of a hydraulic unit in a remote area

would not be user-repairable, prob-

ably not even technician repairable,

and that it would involve shipping

the part back to be repaired in a

controlled environment. The linear

unit has parts that, by a savvy boat

owner, could be swapped or re-

paired on board. We chose the Type

2 Long Linear Drive, for boats up

to 44,000 pounds. Certainly over-

sized but everything on our boat is

built to easily go the distance.

Controller

The Controller (Figure 3) is the

small box in the cockpit with but-

tons for controlling the direction

of the boat. We chose the simplest

controller with the least user op-

tions: the ST6002.

installation

When I looked into the big void

I had made by removing the pro-

pane locker at the back of the boat,

I could not visualize in what direc-

Figure 3

Blue Water Sailing • www.bwsailing.com

tion the tiller arm would extend

from the rudder shaft or where the

linear drive would mount and how

the two would meet and support

themselves in mid air. Our techni-

cian finally stepped aboard carrying

a shiny bronze tiller arm (Figure

4). The tiller arm is a stubby,

strong, bronze lever that bolts onto

the rudderpost. I had previously

measured the rudderpost with a dial

caliper (Figure

5) and ordered

the 10-inch

arm our techni-

cian requested.

Edson tiller

arms are avail-

able in 10-inch

and 15-inch

lengths. Edson

milled the collar

of the tiller arm

according to my

measurements to

fit exactly over

the rudderpost,

and they allow a .006-inch

clamping action onto the rud-

derpost. This tight clamping

to the rudderpost is necessary

for optimum strength. If too

tight, however, the clamp

could bend. Too loose and the

arm could work loose or drop.

Normally when ordering the

tiller arm, you indicate not only

the exact size of the rudderpost

but also mark on the order form

where Edson should cut the key-

way and the size of the keyway.

We had a difficult installation so

we first had to lay out our instal-

lation then mark the collar of the

tiller arm where Edson would

mill the keyway. Edson is very

accommodating; the one thing

Edson can’t help you with is if

you are unlike our technician and

myself and do not have a very

low personal displacement to

length ratio. A husky person would

have a very difficult time mousing

around in all the tight lockers and

recesses to complete the installation.

If you intend on hiring a profes-

sional to do the installation, you

should be well informed of each

step that needs to be performed.

As in any business an installer can

make mistakes or simply cut cor-

ners, which could affect the ulti-

Figure 4

Figure 5

mate operation of the autopilot.

Our technician slipped into the

large hole and I handed him the

tiller arm. He loosely clamped the

tiller arm onto the rudderpost.

Then I lowered to him the Rayma-

rine linear drive unit. Balancing the

tiller arm and linear drive into their

rough positions, the layout and

placement of parts took shape, and

I could see what the steps of my

project would be. He was the layout

man; I was the labor (Figure 6).

Because of the enlarged cockpit

drains I installed on Brick House,

there was no room to mount the til-

51

BRICK HOUSE: AUTOPILOT

It could be possible to

mount the autopilot

directly to the steer-

ing quadrant as long

as it is a bronze case

quadrant. Never attach

a drive unit directly to

an aluminum radial or

quadrant as this could

cause the quadrant to

fail. If you want your

autopilot to be a truly

independent back up

steering system then

use an Edson tiller

arm.

With the rudder

centered, the tiller arm

loosely clamped to the

rudderpost and the

this could damage the drive.” Our

technician left one inch of potential

movement in the push rod in both

directions before the steering hit its

end stops. Now we were ready to

mark on the collar the spot cor-

responding with the keyway on the

rudderpost. This is where Edson

would mill the keyway in the collar.

All this set up left the tiller arm to

be positioned slightly to port of

the rudderpost rather than directly

astern of the rudderpost. It does not

matter where the tiller arm attaches

as long as it is perpendicular to the

drive when the steering wheel is in

the centered position.

If it is not possible to locate a til-

ler arm over a keyway, two pinbolts

could be threaded in the collar and

Figure 6

push rod of the drive

unit halfway extended,

our technician set

holes drilled into the rudderpost

for the bolts to set into. The holes

in the rudderpost should be as

ler arm and drive assembly forward

of the rudderpost and above the

steering quadrant, which would

normally be the most likely place to

do so (Figure 7). The only place to

install the assembly was aft of the

rudderpost and below the steering

quadrant. The steering quadrant is

the big metal bracket bolted to the

rudderpost, which the boat’s steer-

ing cables are attached to. In some

boats, the “quadrant” is not one-

quarter of a circle but a full 360-de-

the drive unit

perpendicular

to the tiller arm

and found where

the base of the

drive unit would

be mounted

to a bulkhead.

This relationship

also gave us the

hole along the

tiller arm for

attachment of

52

gree disk and is called a radial drive.

the drive. Ad-

Figure 7

ditionally, when

setting this up

we had to plan

for the rudder

movement to be

“limited by the

steering system

end stops before

the push rod

reaches its end

stop (Figure 8).

Failure to do

Figure 8

deep as the diameter as the bolts

used. Drilling into stainless steel or

Monel with a hand drill, while con-

torted over bone bruising hard spots

is not an easy proposition. The drill

bit must turn slowly and be cooled

with oil. Allowed to heat up it will

further harden the metal and make

it more difficult to drill into.

The drive is not waterproof so it

must be mounted in a dry location.

The drive base can be mounted

Blue Water Sailing • December 2007

flat, sideways, upside down, it does

not matter. The important thing

is that the push rod of the drive

must operate in the same plane of

travel as the tiller arm. So it is very

import, vertically, where the drive

base mounts. If there is an error, it

cannot be more than five degrees

out of plane, otherwise the ball end

fitting could bind with the tiller

arm (Figure 9). The next important

thing is for the drive to rest parallel

with its mounting base (Figure 10).

This is structurally the best way for

the mounting surfaces to absorb the

tremendous forces exerted on them.

There are the instructions then

there is reality. The forces exerted

by our installation would not be a

sheering force but would be applied

at an angle to the bulkhead. My job

would be to beef up the mounting

bulkhead so the drive will not be

ripped out of its footing or rotate

unexpected parts of the boat. Our

Figure 9

Figure 10

technician had the easy part and

went away to have Edson mill the

keyway on the tiller arm. We are

fortunate to have the Edson factory

located nearby but any machine

shop can mill the keyway.

The existing bulkhead we are

using for mounting the base of the

linear drive is three-quarters-inch

plywood, glassed to the hull and

supported by adjoining bulkheads.

To make sure the plywood does not

flex and to further spread the loads

to the adjoining structure, I sand-

wiched the plywood with quarter-

inch aluminum plates.

Looking in the phone book

under “Steel,” I found a metal

supply company that could sell the

aluminum sheets cut to my rough

dimensions. To make the plates fit

exactly to the contours of the hull

I had made cardboard templates.

Tracing the templates onto the

sheets of aluminum left a line to be

cut with a jig saw. For fine fitting

the aluminum, a

disk sander ground

down the projec-

tions for a perfect

fit. Before installing,

the aluminum was

primed on all sides.

This was done as

much for cosmetics

as well as oxidation

protection since this

was not anodized

aluminum.

Setting the plates in position, I

applied a heavy bead of 3M 5200

sealant to the perimeter of the alu-

minum. Although this is supposed

to be a dry area, I wanted to make

sure no water ever gets between the

plywood and the aluminum. The

sandwich was held together with

clamps till holes were drilled and

the stainless steel bolts were screwed

down tight. When our technician

saw the mounting bulkhead (Figure

11), his comment was “Bullet

proof!”

Fluxgate Compass

Ideally, the fluxgate compass

would be mounted in the boat

where movement is the least. That

would put it in the middle of the

cabin floor near the mast. Since we

can’t be stumbling on the thing, the

floor gets wet and there are bilge

pumps and other wiring nearby, the

search for the best mount expanded

out from that spot. All electrical

wiring, stereo speakers, pumps,

motors, keel bolts and ferrous metal

must be at least three feet away

from the compass. Suddenly our

options were greatly reduced to two

locations. We had the plate cabinet

high in the galley near the center-

line of the boat or low in a forward

hanging locker. We chose the hang-

ing locker location simply because

it was far easier to run concealed

Figure 11

Blue Water Sailing • www.bwsailing.com

53

BRICK HOUSE: AUTOPILOT

54

Figure 12

wiring from that point to the course

computer. Although this is a good

location, we now cannot use metal

hangers in this locker.

Course Computer

The course computer was mount-

ed near the rest of the electronics

in the chart table area, however the

course computer needs to be kept at

least three feet away from speakers,

motors, pumps and high current

carrying cables. These items could

have a magnetic field that can influ-

ence the Gyro Sensor in the course

computer. Cables from the rudder

position sensor, fluxgate compass,

controller and drive all connect

to well labeled and color coded

connections on the bottom of the

course computer. This is a real plug

and play operation.

Control heaD

The 6002 Control Head was set

into the cockpit coaming within

easy reach of the helm. Factory

supplied color coded wires simply

plugged into the back of the control

head then snaked through the boat

to plug into the bottom of the

course computer.

Next came the wiring to power

the linear drive. The power source

begins at a new 40-amp circuit on

the breaker panel. A radio fre-

quency noise suppressing ferrite

supplied with the autopilot was

installed on the new

power wire at the

course computer.

The linear drive

consumes an average

of 48 to 72 watts

at 12 volts, or four

to six amps. There

are simple tables to

determine the gage

wire needed for the

round trip length

from the course

computer to the linear drive.

Whenever in doubt go with the

heavier wire. The only consequence

for this is financial. Using too small

of wire, the consequence could be

a fiasco. An undersized wire may

not carry the required amperage

resulting in melted wires or energy

starved, burned-out equipment.

Near the linear drive, the cables

were terminated at bolt terminals.

This is where the smaller wires from

the linear drive will connect. At

these junctions (Figure 12), a mois-

ture drip loop should be made in

the wires to shed water away from

the connections. Since these cables

will carry a lot of electricity, they

should be located at least three feet

away from any VHF radios or radio

cables. For SSB transmitters or their

cables, the autopilot power cables

should be no closer than seven feet.

Sometimes this just is not practical

so the autopilot might have to be

turned off when transmitting on

the radio, or you could install an

expensive and complex grounding

system throughout the vessel.

ruDDer position sensor

Once the freshly milled tiller arm

was back on the boat, I was able to

install it, bolt the drive base to the

bulkhead and complete all the me-

chanical and electrical connections.

The only installation left to do

was the rudder position indicator

Figure 13

(Figure 13). Using plastic (PVC), I

made a shelf for the rudder sen-

sor to mount on and screwed the

shelf to a bulkhead. The pivot point

of the sensor has to align with

the rudderpost, so the arm of the

indicator will move parallel with the

tiller arm. A threaded rod connects

the indicator to the tiller arm. The

electrical wire from the sensor plugs

into the course computer.

After five days of work the instal-

lation was complete. We switched

on the power and the most amazing

thing happened, it all worked per-

fectly! The boat was ready to move

out of the slip and put the autopilot

through the short commissioning

process, which includes compass

calibration and auto learn.

Besides our technician, this job

was successful because of the full,

patient support from the people

at Edson and Raymarine. We are

ready to sail out of the marina, take

two rights and head for Panama,

2,400 miles south.

Patrick and Rebecca Childress have

restored their 1976 Valiant 40 and have

just left on their circumnavigation. Follow

their adventures through boat projects and

exotic ports regularly in BWS.

Blue Water Sailing • December 2007